## Slide 1: SDR on Hack RF One

## Slide 2: HACKRF One
HackRF One from Great Scott Gadgets is a Software Defined Radio peripheral capable of transmission or reception of radio signals from 1 MHz to 6 GHz. Designed to enable test and development of modern and next generation radio technologies.

## Slide 3: HACKRF One Features
HackRF One is an open source hardware platform that can be used as a USB peripheral or programmed for stand-alone operation.
1 MHz to 6 GHz operating frequency
half-duplex transceiver
up to 20 million samples per second (ADC Clk)
8-bit quadrature samples (8-bit I and 8-bit Q)
compatible with GNU Radio, SDR#, and more
software-configurable RX and TX gain and baseband filter
software-controlled antenna port power (50 mA at 3.3 V)
SMA female antenna connector
SMA female clock input and output for synchronization
convenient buttons for programming
internal pin headers for expansion
Hi-Speed USB 2.0
USB-powered
open source hardware

## Slide 4: HACKRF One Architecture

## Slide 5: Time Domain
Amplitude values over time
Signals are continuous in the air or wire
Signals are digitized by sampling the current value many times

## Slide 6: Discrete Sampling
Usually data is displayed as if it were continuous
  Easier to visualize
  Mostly accurate as long as you follow Nyquist’s Sampling Law
Can also display actual data points
  Select Stem Plot under the Config menu in QT GUI Time Sink

## Slide 7: Complex Sampling
Hard to make fast ADC/DACs When mixing a signal with a sinewave crossing zero you lose all the information!
Solution: Split the signal in two, mix with a sine and cosine, sample each result at the same time
  Twice the information, all of it useful
  Not cheating Nyquist
  Bandwidth = Sample Rate

## Slide 8: Amplitude Modulation
Changing the amplitude of a “carrier” wave at a fixed frequency.

## Slide 9: Modulation Techniques HACKRF One is capable of
Some of them are as follows:
AM (Amplitude Modulation)
ASK (Amplitude Shift Keying)
FSK (Frequency Shift Keying)
BPSK (Binary Phase Shift Keying)
QPSK (Quadrature Phase Shift Keying)
OQPSK (Offset Quadrature Phase Shift Keying)
NBFM (Narrowband Frequency Modulation)
WBFM (Wideband Frequency Modulation)
SSB LSB (Single Sideband Lower Sideband)
SSB USB (Single Sideband Upper Sideband)

## Slide 10: Modulation demos
https://github.com/raam96/HackrfONE_RTLSDR_demo

## Slide 11: ASK Modulation and Demodulation
https://www.researchgate.net/figure/GRC-flow-graph-for-ASK-modulation-and-demodulation_fig16_338436204
Transmittion and reception of BPSK signal using HackRF One anMod RTL-SDR over the air.
https://www.youtube.com/watch?v=SiHD7z2IMVg
Over the air transmittion and reception of QPSK signal using HackRF One and RTL-SDR with GNU Radio.
https://www.youtube.com/watch?v=IAIOsX7S8xo

## Slide 12: User Manual and Documentation
A bit spread out and wanting in depth in spots
User Manual: www.gnuradio.org/doc/doxygen
  Generated from the C++
  Useful for finding out more about blocks
  Talks about the design of the core engine and code
Python Manual: www.gnuradio.org/doc/sphinx
  Generated from the Python
  Does not cover many of the topics in main manual
  Likely to be combined with the C++ in the next year
  Wiki: http://wiki.gnuradio.org
  Several sets of tutorials ○ Presentations from other classes and events
  Working groups and developer info
  GNU Radio Conference info
    Links to videos and slides from the talks
  Lots of outdated pages, getting cleaner over time